## Slide 1
Within-hand Manipulation Planning and Control Approaches for Variable Friction Fingers
Gokul Narayanan(RBE), Joshua Amrith raj(RBE), Abhinav Gandhi(RBE), Aditya A.Gupte(RBE)
Advisors: Profs. Berk Calli, Adam J.Spiers
Abstract
Background
Project Objectives
Develop methods to solve within hand manipulation task.
Evaluate the methods based on path smoothness, accuracy and efficiency by testing on VF Finger Gripper system.
Conclusion and Future directions
Hybrid Method performs faster and gives smoother paths even with inaccurate models of the system as it combines the advantages of the pre-defined path from motion planner and online error correction from visual servoing.
In our future work, we propose to learn the policies to manipulate any object without modelling them explicitly.
Methodology
Each method was tested on 3
different tasks and 5 different start and goal positions.
Tasks:
Perform only position correction.
Perform both position and orientation correction.
Perform Position and orientation correction with modelling inaccuracy.
Evaluation Metrics
Accuracy
Time taken
Path length
Path smoothness
Experiments
Modelling
Visual Servoing:
Motion Planner:
Modified A* search
Cost Function Design:
Results
References
A. J. Spiers, B. Calli, and A. M. Dollar, “Variable-friction finger surfaces to enable within-hand manipulation via gripping and sliding,” IEEE Robotics and Automation Letters, vol. 3, no. 4,pp. 4116–4123, 2018.
B. J. Cohen, S. Chitta, and M. Likhachev, “Search-based planning for manipulation with motion primitives,” in IEEE IntConf on Robotics and Automation (ICRA), 2010, pp. 2902-908.
Develop an Offline Motion planner.
Develop an Online Visual Servoing method.
Develop an Hybrid method integrating offline and online approaches.
The ability to conduct within-hand manipulation provides significant dexterity and flexibility advantages to robots operating in unstructured and constrained environments, as they can re-position and re-orient objects without regrasping. This is a challenging task even for an highly articulated robot. Here we propose different strategies to perform within hand manipulation of objects using Variable Friction(VF) Finger gripper system.
VF Finger Gripper is a 2-DOF robot gripper that can change the effective friction of its finger surfaces with a simple actuated mechanism. It is a non-holonomic switching system which can slide and rotate objects within hand by varying the friction surfaces and the finger angles.
CAMERA
ORIGIN ARUCO MARKER
OBJECT ARUCO MARKER
OBJECT
VF SYSTEM
Trajectory tracked by the object from start pose (7,7,0) to goal pose (12,12,0) for different methods a) Visual servoing b) Offline motion planning c) Hybrid method
Experimental Trajectory
Task Evaluation
fw – Finger Width
Wo – Object dimension
θL, θR – Left and Right actuator angles
dL, dR – Object Position in left and right finger
wp - Width of palm
Experimental Setup
Kinematic Modelling Parameters
Operational Block Diagram